Before acquisition, installation and use of UVC sources a risk assessment of the installation must be conducted. The assessment should be conducted in consultation with the local radiation protection coordinator.

This checklist is meant as a tool for risk assessment and the implementation of necessary safety measures.

| Date: |  | Signature (s): |  |
| --- | --- | --- | --- |

| Points to consider | Follow-up | Responsible for the follow-up | Deadline |
| --- | --- | --- | --- |
| Radiation protection and operation Who is the local radiation protection coordinator? Who is responsible for inspection and maintenance of the installation? Who is responsible for the room? |  |  |  |
| Training/information Who will provide the training? Any particular risk factors associated with unskilled users? Providing informing for others in the vicinity Correct use and maintenance of protective equipment |  |  |  |

| Points to consider | Follow-up | Responsible for the follow-up | Deadline |
| --- | --- | --- | --- |
| Routines and procedures How to provide protection for those who work in or may have access to rooms with open UVC radiation? Start-up/shut-down procedures Emergency situations/preparedness Who will be notified in cases where alarm is sounded, and how? How will others in the vicinity be notified? Operation- and maintenance manuals in Norwegian? Inspection and maintenance |  |  |  |
| Documentation Provisions for writing logs Notifying the local and central radiation protection coordinators? Should a more thorough risk assessment of the UVC installation be conducted, including the risks associated with incorrect use and the consequences in terms of exposure? |  |  |  |
| Location Can the radiation from the UVC source potentially influence close-by areas and equipment? Conditions of ownership and responsibility in relation to rooms and equipment Cleaning – special precautions needed? If so, contact the cleaning section of the Technical Division |  |  |  |

| Points to consider | Follow-up | Responsible for the follow-up | Deadline |
| --- | --- | --- | --- |
| Safety Safety switches on doors or elsewhere; or other devices that will switch off the UV source in the event of somebody entering the room/radiation field? Necessary shielding of the source; encasement? Are radiometers available? For mobile installations: How to ensure adequate safety? How to store UVC tubes in order to prevent incorrect use? The danger of explosion associated with high-pressure lamps |  |  |  |
| Labelling/signposting UVC warning sign outside doors Light or sound signal outside door(s) when the source is in active use? Sufficient information on room-cards? |  |  |  |
| Personal protective equipment Purchase UVC adapted goggles; existing UVC adapted goggles? Wear and tear, weak points, age, labelling Gloves Clothing providing total coverage of skin (long sleeves etc.) |  |  |  |